## Slide 1: RoadPro
Complete User Manual
Every command and every setting, step by step from start to finish
Version 3.3 · 12 October 2026
Type
RDP
to build a road
One road, three edge treatments
BARRICADES
TRAFFIC CONES
KERB STONE
50
!
STOP

## Slide 2: What is inside this manual
CONTENTS
A
Getting started
Slides 3 – 8
What RoadPro draws, new in 3.3, install, commands, workflow, drawing setup
B
Build the road · RDP
Slides 9 – 18
Step by step, the dialog, every setting, barricades / cones / kerb, layers
C
Curves, signs, markings, sections
Slides 19 – 22
RDRAD, RDSEC, signage, RDM road markings, RDX cross sections
D
Widen and taper
Slides 23 – 25
RDW lane widening, both sides, chainage input, RDT road taper
E
Junctions · RDJ
Slides 26 – 29
Step by step, settings, corner barricades / cones / kerb, aux lane, island
F
Single line · RDL (new)
Slides 30 – 31
One run of barricades, cones or kerb stone on any line
G
Report · RDR
Slides 32 – 33
Command line summary, Excel (CSV) file and drawing tables
H
Reference
Slides 34 – 37
Worked example, standard values, troubleshooting, quick reference

## Slide 3: One centre line in, a complete road drawing out
PART A · GETTING STARTED
TIE-IN
0+000
0+020
0+040
0+060
0+080
0+100
30
STOP
!
SG-01
R=10
R=10
ROAD-02
ROAD-01
REPORT + EXCEL
1
2
3
4
5
6
7
8
9
10
1
Tie-in or road closed end
E / N on the tie-in line, or barricade + ROAD CLOSED board
2
Edge treatment
Barricades, traffic cones or kerb stone, per side
3
Road surface and markings
Hatch, white centre line, yellow L4 edge lines, arrows
4
Cones / kerb anywhere
Same units, also in junction corners and RDL single lines
5
Signs with IDs
Speed, warning, road works, STOP / GIVE WAY, sign schedule
6
Centre line + radius
CL linetype, R, TC / CT, curve data, straights S1, S2
7
Junction (RDJ)
Branch road, kerb returns, corner treatment, aux lane, island
8
Chainage
Ticks and labels at your interval from your start chainage
9
Widening and taper
RDW extra lane, RDT width change, treatment follows
10
Report
Quantities, setting-out E / N, sign schedule, Excel file

## Slide 4: What is new in version 3.3
PART A · GETTING STARTED
NEW COMMAND
RDL · Single line
Place one run of barricades, traffic cones or kerb stone along any line, polyline, arc, spline, circle or ellipse. Centred, offset left, right or both sides, from / to distance, quantity label. See slides 30 – 31.
RDJ
Junction corner treatment
A new Corner treatment setting: Same as main road, Barricades, Traffic cones or Kerb stone around the kerb returns. The count is printed and added to the road. See slide 28.
RDW · RDT
Cones and kerb follow changes
Lane widening and road taper now move traffic cones and kerb stone to the new edge, not only barricades. Removed units are taken out of the count.
RDP · RDR
Kerb units and cone band
Kerb stone is drawn as separate units (outline per unit, layer ROAD-KERB). Cones get their white reflective band on ROAD-CONE-BAND. Report shows cones (nos) and kerb (m) per side.
Upgrading from 3.2? Load the new RoadPro.lsp with APPLOAD (replace the old file in the Startup Suite). Your saved settings are kept. Roads drawn with 3.2 work with every 3.3 command.

## Slide 5: Install and load RoadPro
PART A · GETTING STARTED
1
Copy the file to a fixed folder
Save RoadPro.lsp in a folder that will not move, for example C:\RoadPro\
2
Type APPLOAD in AutoCAD
Browse to RoadPro.lsp, select it and press Load. Close the dialog.
3
Check the load message
The command line shows Road Pro v3.3 loaded with all the short commands.
4
Load it every time (recommended)
APPLOAD → Startup Suite → Contents → Add → pick RoadPro.lsp → Close.
5
Security warning?
Choose Always Load, or add the folder in OPTIONS → Files → Trusted Locations.
6
Start working
Type RDP and press Enter. The ROAD PRO dialog opens.
Command: APPLOAD
RoadPro.lsp successfully loaded.
Road Pro v3.3 loaded. ROADPRO (RDP) = build road
ROADREPORT (RDR) = report | ... |
ROADLINE (RDL) = single line
Developed by https://www.exceltokml.com/
Requirements
Full AutoCAD 2014 or newer on Windows (also Civil 3D, Map 3D). AutoCAD LT cannot run LISP.
Drawing in metres (1 unit = 1 m) or millimetres (1 unit = 1 mm).
Settings are remembered between sessions on this PC. ROADPRORESET restores the defaults.
Every command is one UNDO step: type U to take back a whole run.

## Slide 6: All commands and short keys
PART A · GETTING STARTED
Short | Full command | What it does | You select
RDP | ROADPRO | Build a complete road from a centre line (dialog with all settings) | Pick points, or an existing line
RDR | ROADREPORT | Report on screen, Excel (CSV) file and tables in the drawing | Road centre line
RDRAD | ROADRADIUS | Radius, TC / CT and curve data labels on every curve | Road centre line
RDSEC | ROADSECTIONS | Straight sections S1, S2 ... with length, area, chainage, bearing | Road centre line
RDX | ROADXSEC | Cross sections: typical, at one chainage, or at every interval | Road centre line
RDW | ROADWIDEN | Extra lane (widening) with tapers, one side or both sides | Road centre line
RDT | ROADTAPER | Change the road width from a chainage onward | Road centre line
RDJ | ROADJUNCTION | Join a branch road: kerb returns, corner treatment, signs, aux lane, island | MAIN road centre line
RDM | ROADMARK | Draw or remove road markings | Road centre line
RDL | ROADLINE | NEW Single line of barricades, cones or kerb stone on any line | Lines, polylines, arcs, splines
— | ROADPRORESET | Restore every setting to the default values | —
Tip Type the short or the full name. Enter or Space repeats the last command. Only roads built by RoadPro carry the data the other commands need: select the red CL on layer ROAD-CL.

## Slide 7: The workflow from start to finish
PART A · GETTING STARTED
1
APPLOAD
Load
Load RoadPro.lsp once, or keep it in the Startup Suite
›
2
RDP
Build the road
Settings, centre line, then everything is drawn
›
3
RDRAD
Check curves
Radius labels (and RDSEC straights) if not added in RDP
›
4
RDW
Widen / taper
Extra lanes (RDW) and width changes (RDT)
›
5
RDJ
Junctions
Join branch roads with kerb returns and corners
6
RDL
Single lines
Lane closures, work zones, kerb on any line
›
7
RDM
Markings
Draw or redraw markings when needed
›
8
RDX
Cross sections
Typical, one chainage or every interval
›
9
RDR
Report
Run last: quantities, setting-out, Excel
Run RDR last The report reads everything stored on the centre line, so it includes widenings, tapers, junctions and markings. RDL lines are separate: their totals print on the command line and in the label.

## Slide 8: Before you start: prepare the drawing
PART A · GETTING STARTED
Checklist
Units. Decide 1 unit = 1 m (default) or 1 unit = 1 mm and set Drawing units in RDP. Values in all dialogs are always typed in metres. RDL uses the same setting.
Direction. Draw the centre line in the chainage direction. The first point is the start chainage.
One object. Use one Line, Arc or 2D (LW) Polyline with straight and arc segments. Join pieces first with JOIN; explode blocks.
Survey points. Turn on OSNAP and snap the CL to your design or survey points.
Space and UCS. Work in model space. RoadPro switches to the World UCS while it runs and restores yours.
Save the DWG. Save before RDR: the Excel (CSV) file is written next to the drawing.
Left and right, and chainage
START 0+000
END
LEFT side
RIGHT side
← traffic
traffic →
Left / right are seen looking along the CL from its start point. Traffic keeps right.
Chainage can be typed as 150 or 0+150, and 1250.5 or 1+250.500.
Chainages are real road chainages: a road that starts at 1+000 has its widening at 1+150, not at 150.

## Slide 9: Build a road step by step
PART B · BUILD THE ROAD · RDP
1
Type RDP and press Enter
The ROAD PRO dialog opens with your last settings.
2
Road Geometry
Road name, width, turning radius, drawing units, centre line input.
3
Road Edge and Centre
Left / right edge, Barricades, Traffic cones or Kerb stone, centre, sizes, shoulder.
4
Signs and Markings
Speed, warning signs, control at tie-in, sign set.
5
Surface, Chainage, Road Ends and Report
Hatch, centre marking, chainage interval and start, end types, report, section.
6
Press OK, then give the centre line
Pick points: click points, A = arc, L = line, U = undo, Enter = finish. Select existing: click the line.
7
RoadPro builds the road
Edges, surface, treatment, markings, signs, chainage, radius, ends. Summary printed.
8
Report and section
Excel saved → pick a corner for tables (Enter skips) → open Excel? → pick a point for the typical section (Enter skips).
Command: RDP
(dialog: settings, press OK)
Draw the road centre line
(Arc option allowed, Enter to finish):
Specify start point: pick
Specify next point or [Arc/...]: pick
Specify next point or [Arc/...]: A
Specify end point of arc: pick
Specify end point of arc or [Line]: L
Specify next point: Enter
====== ROAD PRO - ROAD-01 ======
Road width : 7.30 m ...
Excel report saved : C:\...\ROAD-01_RoadPro_Report.csv
Pick top-left corner for report tables
<Enter = skip>: pick
Open the Excel report now? [Yes/No] <Yes>: Y
Pick point for the TYPICAL CROSS SECTION
centre line <Enter = skip>: pick

## Slide 10: The RDP dialog at a glance (default values shown)
PART B · BUILD THE ROAD · RDP
ROAD PRO - Road Builder for AutoCAD v3.3
1
Road Geometry
Road name / ID:
ROAD-01
Road width (m):
7.30
Turning radius:
Match existing
Manual radius (m):
10.0
Radius measured at:
Centre line (CL)
Drawing units:
Meters
Centre line input:
Pick points
☑ Show radius, TC / CT and curve data
☑ Show straight sections (S1, S2...)
2
Road Edge and Centre
☑ Left edge ☑ Right edge
Edge:
Barricades (red / white)
Centre:
Centre line markings
Unit length / cone spacing (m):
2.00
Unit / cone / kerb width (m):
0.50
Paved shoulder (m):
0.50
3
Signs and Markings
☑ Speed limit
30 km/h
☑ Bend ahead before (m)
30
☑ Road works ahead (with plate)
☑ Chevron boards on bends
☑ Keep right at median
☑ Lane direction arrows
At tie-in:
STOP sign
☑ Two-way traffic (signs both ways)
☑ Sizes and distances by speed (HDS)
Sign set:
Temporary
Symbol (m) / Spacing (m):
2.0 / 15
4
Surface and Centre Line
☑ Hatch road surface
Hatch pattern / scale:
SOLID / 1.0
☑ Show CL text in centre line
☑ Road markings (centre + edge)
Centre marking:
Standard L1/L2/L2A
☐ SLOW markings before bends
☑ Delineator posts on curves
5
Chainage
☑ Add chainage ticks and labels
Interval (m):
20
Start chainage (m):
0
Text height (m):
1.0
6
Road Ends and Report
Start end:
Tie-in line
Finish end:
Tie-in line
☑ Report tables + Excel (CSV) file
☑ Typical cross section drawing
Panels 1 – 6 are explained one by one on slides 11 – 17

## Slide 11: Road Geometry settings
PANEL 1 · RDP DIALOG
Setting | Options (default) | What it does
Road name / ID | ROAD-01 | Name on labels, report title and the Excel file name ROAD-01_RoadPro_Report.csv. Use a new name for each road.
Road width (m) | 7.30 | Full carriageway width, edge to edge; half on each side of the CL. Paved shoulder is added outside it.
Turning radius | Match existing (keep CL as drawn) / Manual radius at every bend | Match existing keeps your arcs exactly. Manual puts the radius below into every corner of the CL.
Manual radius (m) | 10.0 | Used only with Manual radius (greyed out otherwise).
Radius measured at | Centre line (CL) / Inner edge (kerb line) | Only with Manual radius. Inner edge: the value is the kerb radius and the CL radius becomes R + half width.
Drawing units | Meters / Millimeters | 1 unit = 1 m or 1 unit = 1 mm. Every value in every dialog is still typed in metres.
Centre line input | Pick points (draw new) / Select existing Line/Pline/Arc | Draw the CL after OK, or click a centre line already in the drawing.
Show radius, TC / CT and curve data | On | Radius arrow and value, TC / CT ticks with chainage, curve data box (same as RDRAD).
Show straight sections (S1, S2...) | On | Extent bar with length, area, chainage range and bearing for every straight (same as RDSEC).
Tip Using a CL from the designer? Keep Match existing. Drawing a quick site road with sharp corners? Choose Manual radius and RoadPro rounds every bend for you.

## Slide 12: Turning radius: the two options explained
PANEL 1 · RDP DIALOG
Match existing
R as drawn
Your arcs are kept exactly as drawn. Corners without an arc stay sharp.
Manual radius at every bend
drawn corner
R
Sharp polyline corners get the Manual radius. Good for quick site roads.
Radius measured at
Width 7.30 m | R typed = 10
At CL: inner edge | 6.35 m
At CL: centre line | 10.00 m
At CL: outer edge | 13.65 m
Inner edge: inner | 10.00 m
Inner edge: CL | 13.65 m
Inner edge: outer | 17.30 m
Use Inner edge when the drawing gives a kerb radius.
Rule The CL radius must be larger than half the road width + paved shoulder + unit width, otherwise the inside treatment folds over itself. Example: 7.30 m road, 0.50 shoulder, 0.50 units → CL radius more than 3.65 + 0.50 + 0.50 = 4.65 m. RoadPro prints a warning if a bend is too tight: increase the radius or reduce the width / shoulder.

## Slide 13: Road Edge and Centre settings
PANEL 2 · RDP DIALOG
Setting | Options (default) | What it does
Left edge / Right edge | Both on | Which sides get the edge treatment. Untick one side for a road along a wall, a fence or an existing kerb.
Edge | Barricades (red / white) / Traffic cones / Kerb stone | What is placed along the edges, outside the paved shoulder.
Centre | Centre line markings (no barrier) / Barricades / Traffic cones | Markings only, or a median of barricades or cones on the CL with KEEP RIGHT signs at each nose.
Unit length / cone spacing (m) | 2.00 | Barricades and kerb: length of one unit. Cones: distance from cone to cone.
Unit / cone / kerb width (m) | 0.50 | Barricade width, cone base size or kerb width (for kerb use 0.15 – 0.30).
Paved shoulder (m) | 0.50 | Paved strip between the carriageway edge and the treatment. Hatched, in the section and in the report. 0 = treatment on the edge.
Where each width goes (half section)
Half road width (7.30 / 2 = 3.65)
Shoulder 0.50
Unit 0.50
CL
Cones and kerb sit in the same place as barricades. In RDX the section shows the right profile automatically.

## Slide 14: How to add barricades, traffic cones or kerb stone
HOW TO
Barricades
1
RDP → Road Edge and Centre
2
Tick Left edge and / or Right edge
3
Edge = Barricades (red / white)
4
Unit length 2.00, width 0.50
5
OK and draw the CL
Red / white units with black outline. Report: red and white units per side. RDX: water-filled or New Jersey profile with its height.
Traffic cones
1
RDP → Road Edge and Centre
2
Tick the sides you want
3
Edge = Traffic cones
4
Unit length = cone spacing, e.g. 3.00
5
Width = cone size, e.g. 0.40
Red cones with a white band (ROAD-CONE, ROAD-CONE-BAND). Report: number of cones per side. RDX: 0.75 m cone.
Kerb stone
1
RDP → Road Edge and Centre
2
Tick the sides you want
3
Edge = Kerb stone
4
Unit length = kerb unit, e.g. 1.00
5
Width = kerb width, e.g. 0.15
Grey kerb units with outline (ROAD-KERB). Report: kerb length in m per side. RDX: kerb with 150 mm upstand.
Median on the centre line
Centre = Barricades or Traffic cones
Treatment follows changes
RDW, RDT and RDJ move or cut it for you
Just one line somewhere?
Use RDL, the single line command (slide 30)

## Slide 15: Signs and Markings settings
PANEL 3 · RDP DIALOG
Setting | Options (default) | What it does
Speed limit km/h | On, 30 | Speed limit sign after each entry. The speed also picks HDS sign sizes, warning distances and L1 / L2 patterns.
Bend ahead before (m) | On, 30 | Bend warning sign before every curve. With HDS on, the distance comes from the speed (50 – 300 m).
Road works ahead (with plate) | On | Road works triangle with a distance plate at the entry of each direction.
Chevron boards on bends | On | Chevron boards on the outside of every bend.
Keep right at median | On | KEEP RIGHT sign at each nose of a barricade or cone median.
Lane direction arrows | On | White lane arrows on the straights (5.0 m or 7.5 m by speed).
At tie-in | STOP sign / GIVE WAY sign / No sign | Control sign before each tie-in end of the road.
Two-way traffic | On | Signs for both directions. Off = one-way: signs one way and NO ENTRY at the far end.
Sizes and distances by speed (HDS) | On | Plate sizes and warning distances from Oman HDS 2017 Sec. 19 by speed. Off = Symbol and Spacing below.
Sign set | Permanent / Temporary (road works) | Permanent: yellow / black chevrons. Temporary: black / yellow road-works style.
Symbol (m) / Spacing (m) | 2.0 / 15 | Size of the sign drawing on plan, and the spacing between signs in a group.

## Slide 16: Surface and Centre Line settings
PANEL 4 · RDP DIALOG
Setting | Default | What it does
Hatch road surface | On | Fills the road between the edges.
Hatch pattern | SOLID | Any AutoCAD pattern: AR-CONC, ANSI31 ...
Pattern scale (not SOLID) | 1.0 | Scale for patterns other than SOLID.
Show CL text in centre line | On | Red CL linetype with the letters CL.
Road markings | On | White centre line and yellow L4 edge lines (same as RDM).
Centre marking | Standard L1 / L2 / L2A | See the three options on the right.
SLOW markings before bends | Off | SLOW written on the road before each bend.
Delineator posts on curves | On | Posts on curves at HDS spacing by radius.
Centre marking options
Standard L1 / L2 / L2A by speed
Double continuous white
Single continuous L2A
Yellow L4 edge lines are drawn in all three cases.

## Slide 17: Chainage, road ends and report settings
PANELS 5 AND 6 · RDP DIALOG
Chainage
Setting | Default | What it does
Add chainage ticks and labels | On | Tick and label at every interval.
Interval (m) | 20 | Distance between chainage marks.
Start chainage (m) | 0 | Chainage of the first CL point. Type 1000 or 1+000.
Text height (m) | 1.0 | Labels, curve data and report tables.
Road Ends and Report
Setting | Default | What it does
Start end / Finish end | Tie-in line | Tie-in line, Road closed or None at each end.
Report tables + Excel (CSV) file | On | Runs the report (RDR) right after the road is built.
Typical cross section drawing | On | Asks for a point to place a typical section (RDX).
STOP
Tie-in line (existing road)
Red dashed line across the road with E / N, plus the control sign (STOP / GIVE WAY) set in panel 3.
ROAD CLOSED
Road closed (barricade + sign)
Barricade across the full width and a ROAD CLOSED board. Use for dead ends and work limits.
None
The road simply ends. Use when another road or drawing continues it.

## Slide 18: Everything on its own layer
PART B · BUILD THE ROAD
Layer | Contents
ROAD-CL | Centre line, red CL linetype (holds the road data)
ROAD-EDGE | Left and right carriageway edges
ROAD-SURFACE | Surface hatch
ROAD-SHOULDER | Paved shoulder hatch
ROAD-BARRIER-RED / -WHITE | Barricade unit fills
ROAD-BARRIER-OUTLINE | Black outline of units
ROAD-CONE / ROAD-CONE-BAND | Traffic cones and white band
ROAD-KERB | Kerb stone units
ROAD-CHAINAGE | Chainage ticks and labels
ROAD-CURVE | Radius, TC / CT, curve data
ROAD-SECTION | Straights S1, S2 ...
Layer | Contents
ROAD-SIGN (-RED -WHITE -YELLOW -BLUE) | Posts, plates and symbols
ROAD-MARKING (-FILL) | White lines, arrows, text
ROAD-MARKING-YELLOW | Yellow L4 edge lines
ROAD-DELINEATOR | Delineator posts on curves
ROAD-TIEIN | Tie-in line and E / N
ROAD-WIDENING | Widening and taper labels
ROAD-JUNCTION | Junction labels, corner R, RDL labels
ROAD-ISLAND | Splitter islands
ROAD-REPORT | Report tables
ROAD-XSEC ... | Cross section parts and text
ROAD-01, ROAD-02 ... | Road name groups
Tip Freeze or turn off layers for clean plots (e.g. ROAD-CHAINAGE). Black outlines look white on a dark screen but plot black.

## Slide 19: Radius and straight sections on the plan
PART C · RDRAD · RDSEC
RDRAD
Every curve
C1
R inner = 10.000 m
R CL = 13.650 m
R outer = 17.300 m
L (CL) = 21.441 m
A = 156.52 m²
Δ = 90°00'00"
Radius line with arrow from the centre point, R on the line, TC and CT ticks across the road with chainage. Layer ROAD-CURVE.
RDSEC
Every straight
S1 STRAIGHT
L = 45.230 m
A = 330.18 m²
CH 0+012.000 - 0+057.230
BRG 45°12'30"
Extent bar with end ticks, label parallel to the road. Bearing is whole-circle from North. Layer ROAD-SECTION.
1
Type RDRAD (or RDSEC)
Select the road centre line on layer ROAD-CL.
2
Labels are added
The command line says how many curves / straights were labelled.
When to use If you switched the labels off in RDP, deleted them, or changed the road with RDW / RDT. Erase the old labels on ROAD-CURVE / ROAD-SECTION first so they are not doubled.

## Slide 20: Signage placed automatically, traffic keeps right
PART C · SIGNS
!
Road works ahead
Entry of each direction
30
Speed limit
One spacing after entry
↱
Bend ahead
Distance by speed
STOP
STOP
Before each tie-in
Give way
Option at tie-ins
No entry
Far end, one-way road
↘
Keep right
Median nose
How each sign is drawn on the plan
30
SG-01
Post and plate. Black dot outside the edge treatment; plate faces the traffic.
Leader, symbol and ID. IDs SG-01, SG-02 ... follow the chainage order.
Sizes. By speed (HDS) or your Symbol size.
Also drawn and reported
Chevron boards on the outside of bends (permanent yellow / black, temporary black / yellow)
ROAD CLOSED boards at closed ends
White lane arrows on the straights, delineator posts on curves
STOP / GIVE WAY on every junction branch (RDJ)
Sign schedule in the report: ID, sign, plate size, chainage, side, facing, post E / N

## Slide 21: Road markings: draw, remove and quantities
PART C · RDM
1
Type RDM
Select the road centre line.
2
Choose Draw or Remove
Road markings [Draw/Remove] <Draw>: press Enter to draw.
3
Markings are drawn
Centre line by your Centre marking setting, yellow L4 edge lines, bend warnings, arrows, SLOW (if on).
4
Remove
Deletes the markings RDM drew and clears their quantities from the report.
Good to know New roads: tick Road markings in RDP and you do not need RDM. RDJ redraws the markings of both roads with the junction gaps and adds turning-area markings.
Line | Use | Pattern / size
L1 | Lane / centre line | 2/6, 3/9, 4/12 m by speed, white
L2 | Warning before bends | 6/2, 9/3, 12/4 m
L2A | No overtaking, bends, approaches | Continuous
L4 | Edge line | Yellow, 120 mm (150 mm over 100 km/h)
L5 | Beside an auxiliary lane | 1 m / 1 m
L5/3 | Across a side road mouth | 600 / 300 mm
L7 | Stop line | Solid line + STOP text (2.1 m)
L8 | Give way | Double broken line + 3.75 x 1.25 m triangle
Arrows | Lane direction | 5.0 m or 7.5 m by speed
Report | Quantities | Length per line type and paint area in m²

## Slide 22: Cross sections with widths, layers and heights
PART C · RDX
1
Type RDX
Select the road centre line.
2
Fill the Cross Section dialog
Choose what to draw and set the values (table).
3
Pick the placement point
Typical / one chainage: point for the CL at finished level. Every interval: top-left corner of the sheet.
4
Sections are drawn
Every interval: 3 per row, up to 60 sections. The note says curve or straight.
2.5%
2.5%
Carriageway 7.30 m
Shows the road’s own treatment: barricade, cone or kerb
Setting | Options (default) | Notes
Draw | Typical / At one chainage / At every chainage interval | Typical = one generic section
Chainage (m) | 0 | For At one chainage; 0+150 allowed
Interval (m) | 20 | For every interval
Crossfall (%) | 2.5 | Carriageway slope
Crossfall type | Camber / One-way falls right / falls left | Camber falls both sides
Verge beyond barricade (m) | 1.0 | Ground shown outside
Pavement layers 1 – 3 | Asphalt 0.05 / Base 0.20 / Sub-base 0.15 | Name + thickness; 0 = not used
Barricade profile | Water-filled / New Jersey, height 1.00 | Used when the edge is barricades
Sign post | On, clearance 1.50, sign 0.90 | Post with height to the plate

## Slide 23: Lane widening step by step
PART D · RDW
1
Type RDW, select the road CL
The dialog shows the road chainage range and width.
2
Side and size
Side Left / Right / Both, Extra width 3.65 m.
3
Where
Start and End chainage of the full-width lane, Taper in 30 m, Taper out 30 m.
4
Shape
Taper type straight or curve; Match point fillet (radius 30 m) or direct.
5
Options and OK
Move barricades (cones and kerb too), lane arrow, labels and dimension.
6
Result
New edge drawn, old edge trimmed, treatment moved, markings and report updated.
Right side widening
taper in
START
END
taper out
+3.65
Setting | Default | Notes
Side | Right | Left / Right / Both sides
Extra width (m) | 3.65 | Width of the new lane
Start / End chainage | 100 / 200 | Full-width part, real chainage
Taper in / out (m) | 30 / 30 | Before start and after end
Fillet radius (m) | 30 | Round match points

## Slide 24: Both sides, different chainages, taper shapes and rules
PART D · RDW · RDT
Both sides with different chainage
Set Side = Both sides. The top block becomes the LEFT side.
Tick Different chainage on right side: the right gets its own width, start, end, tapers and fillet radius.
Untick it and both sides use the same values.
Taper type and match point
Straight (linear) taper: straight line from old to new edge.
Curve (reverse-curve) taper: smooth S-shape.
Fillet at match points: rounds the joins with the fillet radius (labelled R=30).
Direct link: sharp joins, no fillet.
Rules that keep it inside the road
Start – taper in must be at or after the road start.
End + taper out must be at or before the road end.
End must be larger than Start.
Keep junctions away from widened or tapered edges.
Options at the bottom of the dialog
Move barricades to the new edge: barricades, cones or kerb follow the new edge.
Lane arrow in the new lane: white arrow in the widened lane.
Labels, width dimension, match points: text on ROAD-WIDENING with chainages.

## Slide 25: Road taper: change the width from a chainage onward
PART D · RDT
1
Type RDT, select the road CL
The dialog shows the chainage range and the design width.
2
Side
Left, Right or Both sides (default Both).
3
Taper start and end chainage
Default 100 and 130: the width changes over these 30 m.
4
Edge shift per side (m)
+ = wider road, – = narrower road. +1.00 both sides makes 7.30 → 9.30 m.
5
Shape and options, OK
Taper type, match point, fillet radius, barricades follow, labels.
Edge shift +1.00 m both sides
7.30
9.30 to the road end
START 0+100
END 0+130
Setting | Default | Notes
Edge shift per side (m) | +1.00 | – values narrow the road
Different chainage on right | Off | Own start, end, shift, radius
Taper type / match point | Straight / fillet | Fillet radius 30 m
Barricades follow new edge | On | Cones and kerb too
Labels and match points | On | On ROAD-WIDENING
More tapers? The new width continues to the road end. Run RDT again at another chainage to change it again (e.g. back to 7.30).

## Slide 26: Junction / tie-in step by step
PART E · RDJ
1
Build the main road first with RDP
The branch uses your RDP settings for barricades, signs and chainage.
2
Type RDJ, select the MAIN road CL
The Road Junction dialog opens and shows the main road range and width.
3
Joining road (branch)
Branch name ROAD-02, width 7.30, Branch centre line: Draw new or Select existing.
4
Junction settings
Corner radius 10, control STOP / GIVE WAY, corner treatment, turning-area markings.
5
Aux lane and island, then OK
Auxiliary lane on the main road, splitter island on the branch.
6
Draw the branch CL
First point ON the main road CL (snap Nearest), then draw outward and press Enter.
7
Junction is built
Branch road, main edges cut, kerb returns, corners, signs, markings, summary printed.
STOP
ROAD-02
ROAD-01 (main)
R=10
R=10
start the branch here, ON the main CL
Crossroads? Run RDJ once for each side at the same chainage. Several branches (J1, J2 ...) can join the same main road.

## Slide 27: Road Junction dialog: every setting
PART E · RDJ
Setting | Options (default) | What it does
Branch road name / ID | ROAD-02 | Name of the joining road (labels, report).
Branch road width (m) | 7.30 | Carriageway width of the branch.
Branch centre line | Draw new (from main road CL) / Select existing | Draw after OK, or click a line that starts on the main CL.
Corner (kerb return) radius (m) | 10.0 | Radius of both kerb returns.
Control on the branch | STOP / GIVE WAY / No sign | Sign and L7 stop line or L8 give-way line on the branch.
Edge treatment around the corners | On | Places a treatment along both kerb returns.
Corner treatment | Same as main road / Barricades / Traffic cones / Kerb stone | NEW in 3.3: choose what goes around the corners (slide 28).
Road markings in the turning area | On | L5/3 across the mouth, L2A approach, turn arrow, STOP / triangle.
Add auxiliary lane (two taper lines) | On | Extra lane on the main road at the junction.
Lane width / long / short / storage | 3.65 / 60 / 30 / 30 m | Width, approach taper (long), departure taper (short), storage length.
Island / width / length | No island / Kerbed / Painted, 1.5 / 15 m | Splitter island on the branch.

## Slide 28: How to add barricades, cones or kerb stone at junction corners
HOW TO · RDJ
Same as main road
Barricades
Traffic cones
Kerb stone
1
RDJ → select main CL
Open the Road Junction dialog.
2
Tick Edge treatment around the corners
Untick to leave the corners open.
3
Choose Corner treatment and press OK
Same as main road uses the main road Edge; size = RDP Unit length / cone spacing and width.
======= ROAD PRO - JUNCTION J1 =======
Branch : ROAD-02 width 7.30 m
Corner R : 10.00 m
Corners : 14 traffic cones
around the corners
Control : STOP sign

## Slide 29: Auxiliary lane and splitter island
PART E · RDJ
Auxiliary lane on the main road
long taper 60
storage 30
short taper 30
L5 1 m / 1 m beside the lane
Splitter island on the branch
1.5 x 15 m
Kerbed or painted
Setting | Default | Range used | Notes
Lane width (m) | 3.65 | 3.0 – 3.65 | Width of the auxiliary lane
Approach taper, long (m) | 60 | by speed | Entry into the lane, before the junction
Departure taper, short (m) | 30 | by speed | Exit back to the main road
Storage length (m) | 30 | by traffic | Full-width part at the junction
Island width / length (m) | 1.5 / 15 | — | Lanes beside the island under 2.75 m give a warning

## Slide 30: Single line of barricades, cones or kerb stone
PART F · RDL · NEW IN 3.3
Use RDL when you need one run anywhere, without building a road:
Lane closure or cone taper on an existing road
Work zone or excavation boundary
Kerb along a footpath, parking or island edge
Barricades on both sides of a trench or a temporary path
A ring of cones round a manhole (circle)
1
Draw the line
Line, polyline, arc, spline, circle or ellipse on any layer, in the run direction.
2
Type RDL and select
Select one or more objects, press Enter. The dialog opens.
3
Choose type, placement and size
Barricades / Traffic cones / Kerb stone; on the line, left, right or both.
4
Press OK
Units are placed, the quantity label is added, totals print. U undoes the run.
Example: cone taper closing a lane
13 CONES @ 3.00 m
Draw a polyline along the closure, RDL → Traffic cones, On the line, spacing 3.00.
Command: RDL
Select lines, polylines, arcs or splines
for the single line run: 1 found, Enter
====== ROAD PRO - SINGLE LINE ======
Traffic cones : 13
Type U to undo this run in one step.

## Slide 31: Single Line dialog: every setting
PART F · RDL
Setting | Options (default) | What it does
Type | Barricades (red / white) / Traffic cones / Kerb stone | What to place along the selected objects.
Placement | On the line (centred) / Offset to the left / Offset to the right / Both sides | Left / right are seen looking along the line from its start point.
Offset from the line (m) | 0.50 | Distance from the line to the units for left, right and both sides.
Unit length / cone spacing (m) | 2.00 | Length of a barricade or kerb unit, or spacing of cones.
Unit / cone / kerb width (m) | 0.50 | Width of the unit or size of the cone.
From distance along line (m) | 0 | Start the run part-way along the line.
To distance (m, 0 = line end) | 0 | Stop the run before the line end.
Quantity label on the drawing | On | e.g. 24 BARRICADES (12 R / 12 W), 13 TRAFFIC CONES or 48.0 m KERB STONE.
On the line
Offset left
Offset right
Both sides

## Slide 32: Make the report and the Excel file
PART G · RDR
1
Save the drawing
The Excel (CSV) file is written in the same folder as the DWG.
2
Type RDR, select the road CL
Any RoadPro road: main road or branch.
3
Read the summary
Printed on the command line (F2 shows it all).
4
Excel file is saved
ROAD-01_RoadPro_Report.csv next to the DWG.
5
Place the tables
Pick the top-left corner, or Enter to skip the drawing tables.
6
Open Excel?
Yes opens the CSV, No continues. Close it before you run RDR again.
Command: RDR
Select the road centre line: pick
======= ROAD PRO REPORT - ROAD-01 =======
Centre line length : 412.350 m
Road surface area : 3010.16 m2
Edge treatment : Barricades
Barricade units : 418 (209 red / 209 white)
Signs : 14
Excel report saved : D:\Project\ROAD-01_...csv
Pick top-left corner for report tables: pick
Open the Excel report now? [Yes/No]: Y
Remember Run RDR after the last change (RDW, RDT, RDJ, RDM) so every quantity is up to date. Enter at the table prompt only skips the drawing tables, never the Excel file.

## Slide 33: What is inside the report
PART G · RDR
Summary
Road name, date, units, start / end chainage, length, width, edge lengths, surface area, straights and curves, design radius, minimum radius
Edge treatment
Barricade units red / white per side, traffic cones per side (nos), kerb stone per side (m), centre median, unit size, paved shoulder and area
Signs and markings
Signs, chevrons, lane arrows, delineators, sign set; marking lengths per line type and paint area (m²)
Curve data
Each curve: TC / CT chainage, radius, arc length, deflection, centre and TC / CT E / N
Road sections
Every straight and curve: chainage range, length, edge lengths, area, bearing
Setting-out
E / N of CL, left edge and right edge at every chainage interval
Sign schedule
ID, sign, plate size, chainage, side, facing direction, post E / N
Widening, taper and junction
Extra areas, new edge offsets, road width at the end, kerb returns TC / IP / CT with E / N

## Slide 34: From a blank drawing to a finished road with a junction
PART H · WORKED EXAMPLE
1
APPLOAD
Load RoadPro.lsp. Save the drawing as SITE-ROAD.dwg.
2
RDP
Geometry: ROAD-01, width 7.30, Match existing, Meters, Pick points.
3
RDP
Edge: Left + Right, Barricades, 2.00 x 0.50, shoulder 0.50. Centre: markings.
4
RDP
Signs: 50 km/h, HDS on, Temporary, STOP at tie-in. Chainage 20 from 0.
5
RDP
Ends: start Tie-in, finish Road closed. Report and section on. OK.
6
RDP
Draw the CL: 3 straights and an arc, Enter. Place tables, open Excel, place section.
7
RDW
Right side, 3.65 m, 0+100 to 0+180, tapers 30 / 30, fillet 30.
8
RDJ
ROAD-02, 7.30 m, R 10, STOP, corners Traffic cones, aux lane on. Branch from 0+300.
9
RDL
Polyline round an excavation: Barricades, Both sides, offset 1.00.
10
RDX
At every chainage interval, 20 m: pick the sheet corner.
11
RDR
Final report: run on ROAD-01 and on ROAD-02.
Result Complete plan, sections, sign schedule, quantities and setting-out for both roads.

## Slide 35: Standard values used (Oman HDS 2017, Section 19)
PART H · REFERENCE
Sign plate sizes by speed (mm) and warning distance
Speed | Triangle | Circle | STOP | GIVE WAY | Warning
50 | 600 | 600 | 750 | 750 | 50 m
60 | 750 | 750 | 900 | 750 | 75 m
80 | 900 | 750 | 1200 | 900 | 150 m
100 | 1200 | 900 | – | – | 200 m
120 | 1500 | 1200 | – | – | 300 m
Road markings
Line | Use | Pattern
L1 | Lane / centre line | 2/6 - 3/9 - 4/12 m
L2 | Warning (bends) | 6/2 - 9/3 - 12/4 m
L2A | No overtaking | Continuous
L4 | Edge (yellow) | Solid, 120 mm
L5 | Beside aux lane | 1 m / 1 m
L5/3 | Across side road | 600 / 300 mm
L7 / L8 | Stop / give way | Line + STOP / triangle
Delineator post spacing on curves (S)
Radius (m) | 500 | 300 | 200 | 100 | 75 | 50 | 25
Spacing S (m) | 50 | 30 | 20 | 15 | 12 | 10 | 7
Approach tangents 2S, 3S, 6S (max 100 m). Posts 0.30 m beyond the paved shoulder. Sign lower edge 1.5 m above ground (2.1 m over a sidewalk). Warning triangles yellow; chevrons yellow / black permanent, black / yellow temporary; cones red with a white band.
Please note Values follow the Oman Highway Design Standards 2017, Section 19 (GCC manual based). For projects in Qatar, check against the Qatar Traffic Control Manual (QTCM) and your project specification. Every value can be changed in the dialogs.

## Slide 36: Troubleshooting and quick fixes
PART H · REFERENCE
Problem | Fix
Unknown command RDP | Load RoadPro.lsp with APPLOAD. Full AutoCAD only, not AutoCAD LT.
Road is 1000 times too small or too big | Set Drawing units to Millimeters for mm drawings (Meters for m).
"No RoadPro data on this object" | Select the red centre line on layer ROAD-CL of a road built by RDP or RDJ.
Warning: edge treatment tighter than the radius | Increase the radius, or reduce the width, shoulder or unit width (slide 12).
Black outline not visible | Dark screen background: outlines show white but plot black.
Excel file could not be saved | Close the old CSV in Excel, save the DWG, then run RDR again.
Junction not formed | Start the branch exactly ON the main CL (snap Nearest), away from widened or tapered edges.
Auxiliary lane skipped | With its tapers it would run past the road end: move the junction or shorten the tapers.
Widening runs outside the road | Start – taper in and End + taper out must stay inside the road chainages.
Chainage not accepted | Type 100 or 0+100 as a real road chainage (includes the start chainage).
RDL placed nothing | From / To outside the line length, or spacing larger than the line. Set To = 0 for the line end.
Settings look wrong | Type ROADPRORESET to restore all defaults (width 7.30 m, radius 10 m).

## Slide 37: Quick reference: shortcuts and default values
PART H · QUICK REFERENCE CARD
RDP
Build road
RDR
Report + Excel
RDRAD
Radius labels
RDSEC
Straight sections
RDX
Cross sections
RDW
Lane widening
RDT
Road taper
RDJ
Junction / tie-in
RDM
Road markings
RDL
Single line (new)
RDP default | Value | RDW / RDT / RDX | Value
Road width | 7.30 m | Extra lane width | 3.65 m
Manual radius | 10.0 m | Widening tapers | 30 / 30 m
Unit / cone spacing | 2.00 m | Taper edge shift | +1.00 m
Unit width | 0.50 m | Fillet radius | 30 m
Paved shoulder | 0.50 m | Crossfall | 2.5 %
Speed | 30 km/h | Barricade height | 1.00 m
Chainage interval | 20 m | Sign clearance | 1.50 m
RDJ / RDL default | Value
Branch width | 7.30 m
Corner radius | 10.0 m
Corner treatment | Same as main
Aux lane / tapers | 3.65 / 60 / 30 m
Island | 1.5 x 15 m
RDL offset / unit | 0.50 / 2.00 m
RDL To distance | 0 = line end

## Slide 38: Build your next road with RoadPro
Version 3.3 · 12 October 2026 · RoadPro.lsp for AutoCAD
RDP
RDW
RDT
RDJ
RDL
RDM
RDX
RDR
Developed by https://www.exceltokml.com/
Standards reference: Oman HDS 2017 Section 19. Check QTCM and your project specification for Qatar.